## Slide 1: Space Packet Structural Components
PACKET PRIMARY HEADER
PACKET DATA FIELD
PACKET SECONDARY HEADER
USER DATA FIELD
SPACE PACKET
6 octets
1 to 65536 octets
Variable
Variable

## Slide 2: Packet Primary Header – Bit-fields
3
PACKET PRIMARY HEADER
PACKET VERSION NUMBER
PACKET IDENTIFICATION
PACKET TYPE
SEC. HDR. FLAG
APPLICATION PROCESS IDENTIFIER
PACKET SEQUENCE CONTROL
SEQUENCE FLAGS
PACKET SEQUENCE COUNT OR PACKET NAME
PACKET DATA LENGTH
3 bits
1 bit
1 bit
11 bits
2 bits
14 bits
2 octets
2 octets
2 octets
16 bits

## Slide 3: Field descriptions
PACKET VERSION NUMBER:
- ‘000’ identifies data unit as a Space Packet
PACKET TYPE:
- ‘0’ for telemetry (or reporting)
- ‘1’ for telecommand (or requesting)
SECONDARY HEADER FLAG:
- Indicates presence of a Packet Secondary Header
- ‘0’ no Packet Secondary Header
- ‘1’ Packet Secondary Header present
APPLICATION PROCESS IDENTIFIER:
Provides a naming mechanism for the managed data path.
SEQUENCE FLAGS:
- ‘00’ if SP contains continuation segment of User Data
- ‘01’ if SP contains first segment of User Data
- ‘10’ if SP contains last segment of User Data
- ‘11’ if SP contains unsegmented User Data
PACKET DATA LENGTH:
- Contains the length count, C, that is one fewer than the length of the Packet Data Field
PACKET SEQUENCE COUNT OR PACKET NAME:
- Sequential binary count of each Space Packet generated by the user application identified by the APID.

## Slide 4: Packet Primary Header – Byte-fields
3
PACKET PRIMARY HEADER
PACKET VERSION NUMBER
PACKET IDENTIFICATION
PACKET TYPE
SEC. HDR. FLAG
APPLICATION PROCESS IDENTIFIER
PACKET SEQUENCE CONTROL
SEQUENCE FLAGS
PACKET SEQUENCE COUNT OR PACKET NAME
PACKET DATA LENGTH
1 byte:
0x00
1 byte:
0x00 – 0x01
1 byte: 0x00 – 0x01
2 bytes:
0x0000 – 0xFFFF
1 byte: 0x00 – 0x03
2 bytes: 0x0000 – 0xFFFF
5 bytes
3 bytes
2 bytes
2 bytes: 0x0000 – 0xFFFF

## Slide 5: XBNF Grammar

## Slide 6
Bit-field SPP header:
Byte-field SPP header:
XBNF Grammar:

## Slide 7: Screenshot for previous slide
3
PACKET PRIMARY HEADER
PACKET VERSION NUMBER
PACKET IDENTIFICATION
PACKET TYPE
SEC. HDR. FLAG
APPLICATION PROCESS IDENTIFIER
PACKET SEQUENCE CONTROL
SEQUENCE FLAGS
PACKET SEQUENCE COUNT OR PACKET NAME
PACKET DATA LENGTH
1 byte:
0x00
1 byte:
0x00 – 0x01
1 byte: 0x00 – 0x01
2 bytes:
0x0000 – 0xFFFF
1 byte: 0x00 – 0x03
2 bytes: 0x0000 – 0xFFFF
5 bytes
3 bytes
2 bytes
2 bytes: 0x0000 – 0xFFFF
Version
Type
SectionHdr
ProcessId
SeqFlags
SeqCntOrName
DataLength